## Slide 1
POWER DEVELOPMENT · TEAM DAY
Reading the NEM
Five ways the market is changing — and what it means for what we build.
Your pack. Browse the data you're drawn to, argue with it, and come to the room with your own hypothesis — not a summary of what you read.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 2
HOW THIS WORKS
A fast, interactive 40 minutes
0:00–0:05
Set the scene — the premise + how it runs; tables take their topic.
PRESENTER
0:05–0:11
The idea + the long view — read your topic's opening chart and the big idea.
TABLES
0:11–0:27
Dig in — work the data and form a position on the questions.
TABLES
0:27–0:40
Report back — ~2 min a table: the key learning, the number, the surprise.
ALL
Two topics have a live calculator — open the kit at travis-coder712.github.io/studio/nem-team-day and record your scenarios on the worksheet in this pack.
THE ONE RULE FOR REPORT-BACK
Key learnings, not a summary. We want the one or two things you now believe that you didn't before — the key learning, the number that changed your mind, and the surprise. The provocations in this pack are here to push you to a position.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 3
YOUR FIVE PERSPECTIVES
Pick the data you're drawn to
1
Market cycles & shocks
Prices move in shock-driven cycles — and a small $/MWh move is a big move in returns.
2
Increasing renewable penetration
Storage is critical, and its volume climbs non-linearly toward 100% — a little gas tames it.
3
Through the lens of demand
Flat for a decade — could it double? Rooftop hid the growth; shape matters as much as size.
4
The economics of building
The more you build, the less it's worth — until coal leaves. Value cannibalises, then cycles back.
5
Award vs concrete vs electrons
Most of the pipeline is a mirage — proposed, committed and built are worlds apart.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 4
ONE FRAME TO CARRY IN — AND A THREAD TO DAY 2
We go deep on the market because it's the force that moves
A development cycle runs for years; the market cycle turns in months. So today we read the market closely — it swings the most, and it's the one worth re-reading with fresh data. A project sits inside other forces too — policy and support, capital, the asset's own fundamentals — but we already know those reasonably well, so we hold them lightly and keep the lens on the market.
THE THREAD TO DAY 2
Day 2 — “So What?” — picks up right here: having read the market, what do we actually change in how we develop? No need to resolve it now — just hold the thought; it lands tomorrow.
The market is one force among several — today we simply give it the closest read.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 5
TOPIC 1
Market cycles & shocks
Prices move in shock-driven cycles — and because capex is fixed, a small $/MWh move is a big move in returns.
START HERE
Where are we in the cycle right now — a calm, well-supplied moment, or one heatwave and one broken boiler from the next spike?

## Slide 6
TOPIC 1 · MARKET CYCLES
The long view — a decade of prices, and the forward
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | CY27f | CY28f
NSW | 39 | 59 | 96 | 82 | 85 | 60 | 67 | 183 | 96 | 131 | 103 | 74 | 85 | 86
QLD | 52 | 67 | 102 | 75 | 72 | 41 | 93 | 205 | 91 | 112 | 85 | 66 | 75 | 74
SA | 50 | 81 | 105 | 100 | 99 | 44 | 45 | 156 | 80 | 100 | 87 | 87 | 80 | 92
VIC | 34 | 47 | 92 | 91 | 109 | 52 | 36 | 134 | 55 | 82 | 78 | 49 | 62 | 71
TAS | 48 | 96 | 98 | 74 | 94 | 43 | 32 | 147 | 56 | 96 | 96 | 90
Takeaway 2022's gas shock towers over the decade; the last two points (CY27–28f) are the ASX forward — low and flat.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 7
TOPIC 1 · MARKET CYCLES
The data on the table
▸ NSW wholesale: $60 (2020) → $183 (2022) → $74 (2026 YTD); QLD hit $205 in 2022 — 5× 2020.
▸ June 2022: the NEM was suspended for the first time ever; the price cap held prices at $300.
▸ Spike-hours (≥$300): NSW 1,393 in 2022 → 9 in 2026 YTD. The cap itself climbed $15k → $20k.
▸ ASX forward (CY27–28): NSW ~$85, VIC ~$62–71 (cheapest), SA in contango to ~$92 — where projects hedge and lenders price risk.
▸ 21 GW of coal still operating; ~6 GW exits 2028–29 (Yallourn, Eraring, Gladstone).
▸ Returns leverage: a $10/MWh swing ≈ +1 pt ungeared yield (~+2.6 pt geared) off a fixed ~$3m/MW capex.
Today's outturns re-rate the forward curve above and the long-term forecasts that underwrite FID.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 8
TOPIC 1 · MARKET CYCLES
Provocations — take a position
A
Is today a calm, well-supplied moment — or one shock from the next spike?
B
What would a repeat of 2022 do to the revenue our pipeline is underwritten on?
C
Given the cycle, when in it would you want a project to reach FID?
D
Does the escalating price cap make merchant exposure more attractive — or just wider?
YOUR HYPOTHESIS
Where do you think we sit in the cycle — and what would you do about timing?
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 9
TOPIC 2
Increasing renewable penetration
Storage is critical, and the volume you need climbs non-linearly toward 100% — a little firm gas tames it.
START HERE
To firm 90% wind + solar you need ~800 big batteries; 100% is a wall. How much gas keeps the number sane?

## Slide 10
TOPIC 2 · RENEWABLES
The long view — storage vs the target
Chart: 
| 30% | 50% | 70% | 80% | 90% | 95%
4-hour “big batteries” needed | 0 | 12 | 51 | 234 | 816 | 1222
Takeaway Storage climbs far faster than linearly near 100%: ~50 batteries at 70%, ~800 at 90%, and 100% is a wall.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 11
TOPIC 2 · RENEWABLES
The data on the table
▸ The NEM is ~44% renewable today (grid wind+solar ~29%, plus hydro and rooftop).
▸ Curtailment roughly doubled to 7.4 TWh in two years; SA solar spills 34% of its output.
▸ Firming 90% ≈ 800 four-hour “big batteries”; 100% can't be done with 4-hr BESS alone.
▸ Least storage lands at a balanced ~40–55% wind mix; the firming sweet spot keeps ~10–12% gas.
▸ Storage now sets the price 31.5% of the time (0.1% in 2015) — as often as all fossil combined.
▸ The objective isn't 0% spill — some is optimal; beyond a threshold, BESS time-shifts it into the evening.
Assumptions (teaching model): wind CF ~34%, solar CF ~32% potential; 4-hr BESS = 500 MW / 2 GWh; demand ~184 TWh.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 12
TOPIC 2 · RENEWABLES
Scenario worksheet — record what you find
Open the live calculator (in the kit) and run these. Writing the outputs down is what makes the knee stick.
Scenario | Target % | Wind % | Overbuild | → Batteries | Storage | Curtail %
Today's stretch (~70%) |  |  |  |  |  | 
A deep build (~90%) |  |  |  |  |  | 
Push to 100% |  |  |  |  |  | 
Least-storage mix |  |  |  |  |  | 
Your own scenario |  |  |  |  |  | 
RECORD YOUR FINDING — THEN A POSITION
The knee bites around ______% renewable. Least storage is at ______% wind. Keeping ~10% gas takes batteries from ______ to ______. My hypothesis on the realistic target: __________________________
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 13
TOPIC 2 · RENEWABLES
Provocations — take a position
A
Where does the storage “knee” bite — and how much gas keeps the number sane?
B
Which wind/solar mix needs the least storage, and why?
C
Is 100% even the right target, or is the last slice a different technology problem?
D
Overbuild-and-spill vs store — where's the crossover for your project?
YOUR HYPOTHESIS
What's the realistic renewable target, and what firms the last mile — storage, gas, or overbuild?
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 14
TOPIC 3
Through the lens of demand
Demand's been flat for a decade — but that flatline hid real growth, and shape matters as much as size.
START HERE
Rooftop quietly hid ~16 TWh of demand growth. Can it keep pace with EVs and data centres — or must the grid finally grow?

## Slide 15
TOPIC 3 · DEMAND
The long view — flat, then the climb
Chart: 
| 2020 | 2022 | 2024 | 2025 | 2026 | 2030 | 2035 | 2040 | 2045 | 2050
Actual | 181 | 178 | 177 | 177
Step Change forecast (2026 ESOO) | 177 | 180 | 197 | 243 | 278 | 305 | 329
Takeaway Operational demand sat flat ~177 TWh; the 2026 ESOO central case bends up ~86% by 2050 to ~329 TWh (the range runs to ~2.8×).
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 16
TOPIC 3 · DEMAND
The data on the table
▸ Operational demand (grid supply after rooftop) was flat ~177 TWh, 2020–25.
▸ But rooftop hid +16 TWh behind the meter (13 → 29 TWh) — underlying use actually rose ~7%.
▸ 2026 ESOO range to 2050: 1.5–2.8×; central Step Change ~329 TWh (+86%) — revised up from the ISP's ~290.
▸ EV load 0.9 → 71 TWh (2026→2050); data centres 5 → 34 TWh (3%→13%); rooftop installs ~2.7 GW/yr.
▸ Reliability: standard forecast exceeded from 2030-31 (NSW/VIC) under committed+anticipated developments.
▸ Push rooftop to ~70 GW and midday operational demand goes negative — the “canyon”.
▸ Demand → price: +1 GW ≈ +$20/MWh — so demand growth is a tailwind to the price cycle.
“Operational demand” = total electricity use minus what rooftop serves behind the meter — what the grid must supply.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 17
TOPIC 3 · DEMAND
Scenario worksheet — record what you find
Open the live duck-curve calculator (in the kit) and run these. Record the belly and the peak — watch the shape move.
Scenario | Rooftop GW | EV TWh | Managed % | Data-ctr GW | → Belly (min) | Peak
Today |  |  |  |  |  | 
A ~2035 build-out |  |  |  |  |  | 
The rooftop 'canyon' |  |  |  |  |  | 
Unmanaged EV charging |  |  |  |  |  | 
Your own scenario |  |  |  |  |  | 
RECORD YOUR FINDING — THEN A POSITION
The belly goes negative at ______ GW of rooftop. Managed → unmanaged EV swings the peak by ~______ GW. My hypothesis — is it a size or a shape problem? __________________________
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 18
TOPIC 3 · DEMAND
Provocations — take a position
A
Can rooftop keep pace with EV + electrification + data-centre load, or does the grid finally grow?
B
Managed vs unmanaged EV charging — how big is the swing in the evening peak?
C
Is the build problem now the evening ramp and midday trough, not annual TWh?
D
Which of the three engines — EV, electrification, data centres — is nearest-term for us?
YOUR HYPOTHESIS
Does demand double — and is it a size problem or a shape problem?
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 19
TOPIC 4
The economics of building
The more you build, the less it's worth — until coal leaves. Value cannibalises, then cycles back.
START HERE
Solar's captured value fell from 1.06× to 0.37× the pool — it did this to itself. Is the trough permanent?

## Slide 20
TOPIC 4 · ECONOMICS
The long view — cannibalisation, and how it cycles
Chart: 
| 2019 | 2021 | 2022 | 2023 | 2024 | 2026
Solar value factor | 1.06 | 0.43 | 0.57 | 0.37 | 0.37 | 0.67
Wind value factor | 0.83 | 0.7 | 0.82 | 0.64 | 0.67 | 0.67
Takeaway Solar's value factor collapsed as it built out — but it cycles: scarcity lifts it, oversupply crushes it.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 21
TOPIC 4 · ECONOMICS
Cannibalisation by state — and the 2026 bounce
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026
NSW | 0.61 | 0.61 | 0.57 | 0.55 | 0.43 | 0.63
QLD | 0.57 | 0.52 | 0.36 | 0.36 | 0.28 | 0.5
SA | 0.43 | 0.5 | 0.37 | 0.44 | 0.53 | 0.67
VIC | 0.43 | 0.57 | 0.37 | 0.37 | 0.34 | 0.57
Takeaway Why 2025 was the trough: +2.8 GW of solar (a record) landed before storage caught up, so midday negative-price frequency roughly doubled (NSW 13→30%, QLD 39→53%). In 2026 new solar paused (+0.3 GW) and ~8 GW of batteries began soaking the midday trough — so capture recovered everywhere (QLD 0.28→0.50, NSW 0.43→0.63). 2026 is YTD, so read the direction.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 22
TOPIC 4 · ECONOMICS
The proof — more batteries, fewer negative middays
The states that added the most midday battery charging in 2026 saw midday negative prices collapse the most — almost exactly in rank order.
State | Batteries added ’25–26 | Midday charging added | Negative middays ’25→’26 | Midday capture ’25→’26
QLD | +3.2 GW | +647 GWh | 53% → 30% (−23) | $14 → $26
NSW | +2.6 GW | +568 GWh | 30% → 11% (−19) | $33 → $43
VIC | +1.9 GW | +287 GWh | 40% → 38% (−2) | $24 → $25
SA | +0.9 GW | +92 GWh | 52% → 48% (−4) | $17 → $27
Read the negative-midday drop — the direct “soaking” signal: QLD & NSW built the most storage and got the biggest recovery. (Absolute prices also eased with a softer 2026 pool; SA's jump is off a tiny base, not battery-driven.) Midday = 9am–3pm, matched Jan–Aug.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 23
TOPIC 4 · ECONOMICS
The battery mirror — spread, not value factor
Chart: 
| Jul-24 | Oct-24 | Jan-25 | Apr-25 | Jul-25 | Oct-25 | Jan-26 | Apr-26 | Jun-26
Top-2hr arbitrage spread | 878 | 326 | 309 | 261 | 350 | 204 | 482 | 116 | 213
Takeaway A battery lives on the price spread. It compressed from ~$500–880 to ~$100–200 as the fleet grew 4 → 60 — but it cycles too.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 24
TOPIC 4 · ECONOMICS
Battery build by state — spread, size & duration
Where the batteries are, how big and how long they last — against the spread they chase.
State | Spread (tb2) | Batteries | Power GW | Energy GWh | Duration | Building GW
NSW | $276 | 17 | 4.1 | 8.7 | 2.1 hr | 3.5
QLD | $188 | 16 | 3.8 | 7.5 | 2.0 hr | 1.1
VIC | $201 | 15 | 2.8 | 4.7 | 1.7 hr | 2.5
SA | $384 | 17 | 1.7 | 2.9 | 1.7 hr | 1.0
NEM | — | 65 | 12.3 | 23.8 | 1.9 hr | 8.0
The tell: SA has the widest spread but the smallest, shortest batteries (power / FCAS-focused); NSW & QLD hold the biggest fleets on thinner spreads. The build pipeline is deeper (2.5–3 hr) — the fleet is lengthening as the easy spread compresses.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 25
TOPIC 4 · ECONOMICS
Battery spread by state, over time
Chart: 
| Jul-24 | Oct-24 | Jan-25 | Apr-25 | Jul-25 | Oct-25 | Jan-26 | Apr-26
SA | 890 | 345 | 382 | 517 | 376 | 234 | 526 | 278
NSW | 439 | 761 | 318 | 685 | 210 | 321 | 203 | 90
QLD | 409 | 603 | 321 | 460 | 200 | 165 | 130 | 99
VIC | 422 | 234 | 219 | 516 | 203 | 157 | 126 | 99
Takeaway SA stays the widest and most volatile; NSW, QLD and VIC have converged toward ~$100 as their fleets filled in.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 26
TOPIC 4 · ECONOMICS
The data on the table
▸ VIC solar value factor: 1.06× (2019) → 0.37× (2023–24 trough) → 0.67× (2026 YTD). It cycles.
▸ Why 2025 was the trough: a record +2.8 GW solar landed before storage caught up — midday negatives ~doubled (NSW 13→30%); 2026's battery wave (~8 GW) soaked it back.
▸ “Darkest before dawn”: worst while coal floods the midday; as coal exits, evening scarcity returns value.
▸ Batteries: top-2hr spread ~$500–880 → ~$100–200 as the fleet grew 4 → 60 — but it spikes in volatile months.
▸ Compression is BESS and benign conditions — coal still in, mild weather, high unit availability.
▸ The fleet: ~65 batteries / 12.3 GW / 24 GWh operating; ~8 GW / 21 GWh committed and building.
▸ FCAS revenue fell ~90–95% in five years — a whole stream competed to near-zero.
Value factor is a generation idea; a battery's analog is the spread. Both erode as you build — and both cycle.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 27
TOPIC 4 · ECONOMICS
Provocations — take a position
A
Is the value-factor trough permanent, or does coal-exit evening scarcity bring it back?
B
Does that change whether — or when — you build, and whether to firm it?
C
The battery spread is compressing — is it BESS, benign conditions, or both? What happens next cycle?
D
Would you build another unfirmed solar farm in this market?
YOUR HYPOTHESIS
Where's the value in 5 years — in energy, or in flexibility?
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 28
TOPIC 5
Award vs concrete vs electrons
Most of the pipeline is a mirage — the gap between proposed, committed and built is enormous.
START HERE
Of 105 GW “proposed” in 2022, only ~9 GW got built. Which signals separate the real projects from the mirage?

## Slide 29
TOPIC 5 · PIPELINE
The long view — the mirage growing
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Proposed | 53 | 53 | 83 | 178 | 250 | 298 | 346
Committed | 6 | 6 | 8 | 10 | 10 | 13 | 13
Built (existing) | 52 | 55 | 57 | 55 | 59 | 61 | 70
Takeaway Proposed capacity multiplied ~7× to 346 GW while committed and built crawled — the gap is the mirage.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 30
TOPIC 5 · PIPELINE
The data on the table
▸ Proposed 346 GW vs committed ~13 GW vs built ~70 GW (2026) — a ~19:1 funnel.
▸ AEMO 2026 ESOO: 9.1 GW connected in 2025-26 (>2× the prior year); ~40 GW committed+anticipated — more than half today's NEM capacity.
▸ Back-test: of 105.7 GW proposed in 2022, only ~9.6 GW built, 52.6 GW dropped by 2026 (~9% conversion).
▸ Even “Committed” isn't concrete: Snowy 2.0 has been committed 4+ years and still isn't built.
▸ CIS: ~32 GW contracted, just 0.29 GW operating — a floor price is not a built asset.
▸ Only 3 major transmission lines are in construction; ~30% of projects draw a full EPBC assessment.
▸ Commissioning takes real time: wind ~10 months, batteries ~7 from first energisation.
The back-test is the crown jewel: “Committed” is a probability, not a promise — and the data can price it.
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 31
TOPIC 5 · PIPELINE
Provocations — take a position
A
Which gate kills the most megawatts — connection, transmission, offtake, or planning?
B
What early signal best separates the real projects from the mirage?
C
Does our screening assume anything remotely as brutal as ~9% proposed-to-built?
D
If you could unlock one transmission line, which frees the most generation?
YOUR HYPOTHESIS
What's the one signal you'll check before believing a “pipeline” number?
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 32
REPORT BACK
Three things — not a summary
The call
Your position on the question — a view, not a recap.
The number
The single figure that changed your mind.
The surprise
The one “I didn't realise that” moment.
Then, as a room:
▸ Is 100% renewable the right target — or do we plan for ~90% + firm gas?
▸ Would you build another unfirmed solar farm in this market?
▸ Heatwave, broken boiler, or data-centre boom — what's the biggest risk to the grid we're building for?
Reading the NEM · Power Development Team Day · figures from the AusEnergy Lens (AEMO + ISP 2026), as-at Aug 2026

## Slide 33
Every figure is real
Sourced from the AusEnergy “Lens” — a live database over the AEMO dispatch decade (2015→2026), the 2026 ESOO + ISP 2026, Open Electricity and the CER. As-at August 2026. The calculators and the storage/leverage figures are transparent teaching models, not planning tools — the point is the shape of the answer.
This is the paper cut. The interactive version holds more — the two live calculators and the full “datasets on the table” for each topic. We'll find a clean way to surface those to the wider team afterwards.
Explore it all live: travis-coder712.github.io/studio/nem-team-day